## Slide 1
WIRELESS NETWORKS
BATCH 2
2024
March, 2024
Vignan University

## Slide 2
ABOUT US
211FA19002 – Y.V. PRANAY KUMAR
211FA19008 – S. VASU VAMSI KRISHNA
211FA19023 – A. BASANTH
211FA19056 – P. SNIKITHA

## Slide 3
Reasons for Using Cellular Systems
To make the best use of the available spectrum, cellular networks employ multiplexing techniques such as frequency division multiplexing (FDM) and time division multiplexing (TDM). This enables the transmission of numerous communications over the same frequency range, eliminating the requirement for additional spectrum and hence cutting the cost of deployment.
02
By dividing the coverage area into smaller cells, cellular systems can provide more reliable service. If a signal is lost in one cell, users can switch to another cell, ensuring continuous communication.
03
Cellular systems are intended to accommodate mobile users. As users move, their devices can automatically switch between cells, ensuring a smooth transition from one to the next.
01
Cellular systems can accommodate a huge number of users at once. As the need for mobile communication increases, cellular systems can be expanded by adding more cells, providing for continuous coverage and service provision.

## Slide 4
02
SDM uses multiple antennas to transmit numerous signals to different users at the same time. Each antenna can transmit a signal to a different user, hence increasing the network's capacity.
03
SDM and FDM can be coupled to boost a network's capacity. For example, each antenna can be utilized to send numerous signals (using FDM) to different users, hence expanding the number of users who can be served at the same time.
01
This approach divides the available frequency spectrum into several narrow bands, each of which can carry a distinct signal. This enables the simultaneous transmission of numerous signals across the same frequency range, hence enhancing network capacity.
SDM and FDM
SDM is typically realized and combined with Frequency Division Multiplexing (FDM) in the following way :
SDM
FBM
Combination

## Slide 5
Dynamic Channel Allocation (DCA) and Frequency Availability
Dynamic Channel Allocation (DCA) is a mechanism used in cellular systems to maximize the utilization of available spectrum. DCA modifies the frequencies available in other cells by altering the frequency bands that each cell may access. By dynamically allocating frequencies, DCA guarantees that each cell has access to the frequencies that are most appropriate for its current needs while minimizing interference with other cells.

## Slide 6
Limitations of TDM/FDM Systems vs. CDM Systems
The comparison of Time Division Multiplexing (TDM)/Frequency Division Multiplexing (FDM) and Code Division Multiplexing (CDM) systems exposes a basic capacity difference. TDM/FDM's reliance on preset channels limits user capacity and might impair service as demand increases, but CDM's unique coding for each user overcomes such constraints, enabling scalable and efficient communication solutions.
TDM/FDM Systems
TDM and FDM systems have a set number of communication channels or slots. This means that the number of concurrent users is determined by the number of channels or slots available. As the number of users grows, the quality of service may suffer due to greater competition for limited resources.
CDM Systems
Code Division Multiplexing (CDM) systems, on the other hand, can handle an almost infinite number of users because each one is issued a unique code. This provides for far larger capacity than TDM/FDM systems because the number of users has no direct impact on the number of channels or slots.

## Slide 7
Impact of Additional Users on Transmission Quality
When the load in a cell grows, meaning more users are attempting to communicate concurrently, the transmission quality can be altered in a number of ways
01
Interference becomes more likely when more users transmit signals at the same time. This can lead to signal deterioration and a lower quality of service.
Interference
02
Each user competes for finite resources (such as bandwidth and power). This can lead to diminished signal strength and delay.
Resource Contention
03
The quality of service for each user may suffer as the network attempts to manage the increasing demand efficiently.
Quality of Service

## Slide 8
01
External sources of electromagnetic radiation can disrupt the signal, causing it to degrade.
Interference
02
As the signal moves through the air, it may lose power owing to absorption, scattering, and other types of attenuation.
Signal Attenuation
03
Background noise can interfere with the signal, making it harder to discern between the intended signal and the noise.
Noise
Transmitting Digital Signals Without Loss
When the load in a cell grows, meaning more users are attempting to communicate concurrently, the transmission quality can be altered in a number of ways

## Slide 9
Main Problems of Signal Propagation
Signal propagation in wireless communication faces several challenges:
01. Fading
Signal strength can vary over time and distance, leading to a loss of signal quality.
02. Multipath Propagation
Signals can take multiple paths to reach the receiver, with some paths experiencing delays and others causing interference.
03. Shadowing
Areas where the signal is blocked by obstacles can lead to signal loss or degradation.

## Slide 10
Why Radio Waves Don't Always Follow a Straight Line
Radio waves do not always follow a straight line due to several factors
01
Radio waves can bend as they pass through different mediums (for example, air and water), causing them to travel along a curved path.
Refraction
02
When radio waves approach an impediment, they might spread out and take a curved route.
Diffraction
03
Radio waves can be deflected by barriers, leading them to diverge from their intended direction.
Scattering

## Slide 11
Reflection in Signal Propagation
Reflection has a dual role in signal propagation, acting as both a friend and foe.
On the one hand, it increases signal reach by reflecting off surfaces.
On the other hand, it can cause interference because reflected signals may collide with direct signals at the receiver.
Harmful
Reflection can also result in interference. If a signal is reflected off an obstruction and reaches the receiver, it may interfere with the direct signal, resulting in signal deterioration.
Useful
Reflection can be utilized to broaden the coverage of a signal. A signal can be reflected off buildings or other structures to reach regions that are not directly in line with the transmitter.

## Slide 12
Thank You
BATCH 2
CYBER SECURITY
III ACSE